## Slide 1: IF ELSE Statements
BY ARVIND SESHAN

## Slide 2: Lesson Objectives
Learn how to make your robot decide what to do out of different choices
Learn how to use an if else statement

## Slide 3: IF ELSE Statements
Asking the robot a question and doing something different based on the answer
Example:
  Does the robot see a line? Or not?
  Is the robot near the wall? Or not?
It is like a yes/no question
An if statement requires an expression with a Boolean output. If the output, is true, the indented code below will run
if expression:
#Code
You can add an else statement after to run code if the expression returns false
if expression:
#Code
else:
#Code 2

## Slide 4: ELIF Statements
Notice that in the last example, the else statement took no inputs. It just ran when the if expression returned false.
The elif statement can be used to check another condition, given the previous condition returned false. elif stands for “else if”.
if expression:
#Code
elif expression2:
#Code 2
Code 2 will only run if expression returns false and expression2 returns true.
You can use multiple if and elif statements in a row, but only one else statement.
if expression:
#Code
elif expression2:
#Code 2
elif expression3:
#Code 3
else:
#Code 4

## Slide 5: Challenge: Happy or Sad?
Write a program that changes the display based on if the Force Sensor is pressed or not pressed
If pressed, your SPIKE Prime is happy. Display a smiley face. On the LED Matrix.
If not pressed, SPIKE Prime is sad! Display a sad face.
You will need to use the Light Functions, a loop, and an If Else Statement.

## Slide 6: Challenge solution
When the Force sensor is pressed, the LED Matrix shows a happy face
When you let go of the Force sensor, the LED Matrix shows a sad face
Run the code forever
force = ForceSensor('F')
while True:
if (force.is_pressed()):
hub.light_matrix.show_image('HAPPY')
else:
hub.light_matrix.show_image('SAD')
Initialize the Force Sensor

## Slide 7: CREDITS
This lesson was created by Arvind Seshan for Prime Lessons
More lessons are available at www.primelessons.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.