## Slide 1: GYRO MOVE STRAIGHT
BY SANJAY AND ARVIND SESHAN

## Slide 2: Lesson Objectives
Learn to apply proportional control to get your robot to move straight
Learn to apply proportional control to the Gyro sensor move at a particular angle

## Slide 3: Tips For Success
You must go through the Proportional Line Follower Lesson before you complete this lesson
You must also complete the Turning With Gyro Lesson

## Slide 4: What is Gyro Move Straight?
Imagine that you want to drive for 200 cm straight
As you travel, your robot gets bumped by something
A gyro move straight program helps the robot correct itself back to straight, but offset by how much it was bumped

## Slide 5: How it Works
Application | Objective | Error | Correction
Gyro Straight | Make the robot at a constant heading/angle | How far you are from that heading/angle | Turn sharper based on how far you are from that angle
Line Follower | Stay on the edge of the line | How far are our light readings from those at line edge (current_light – target_light) | Turn sharper based on distance from line
A proportional line follower and a gyro move straight code share similar properties
To write a gyro move straight program, you must first think about what the error is and what the correction needs to be

## Slide 6: Pseudocode
Set Movement Motors
Reset your yaw value to 0
In a loop, compute the error and apply the correction
  Part 1: Compute Error (How far from target angle)
    To move straight  Target yaw angle=0 (Note: Assuming a horizontal hub placement, we must look at the yaw direction for the angle offset. This may be different for your setup)
    Distance from target angle is just current yaw reading
  Part 2: Compute a Correction that is proportional to the error
    Multiply the Error from Part 1 by a constant (that you must experiment and discover for your robot)
  Plug the value from Part 2 into a move block with each motor adjusted proportionally
Exit loop as required by changing loop block

## Slide 7: Solution: Gyro Move Straight
Reset the yaw angle to set the direction the the robot is trying to stay at.
Start moving and adjust the steering based on how far off the robot is from its target
Loop so that the robot keeps updating its correction
Calculate the yaw error and correction

## Slide 8: Discussion Guide
Compare the proportional line follower code with the proportional move straight code. What similarities and differences do you see? Ans. The code is almost the same. The one difference is how the error is calculated. The error is calculated using the gyro sensor. The correction is identical.
What if you wanted to travel at a particular angle (not just straight)? How would the code look different?
  Ans. In Part 1 of the solution code, there is no subtraction block because we were just subtracting “0” since our target heading is moving straight. You would have to subtract your current angle from the target angle if you wanted to move at some other angle.
Target angle = 5 degrees

## Slide 9: CREDITS
This lesson was created by Sanjay Seshan and Arvind Seshan for SPIKE Prime Lessons
More lessons are available at www.primelessons.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.