## Slide 1: Turning With the Gyro
ARVIND SESHAN

## Slide 2: Lesson Objectives
Learn how to turn using the built-in gyro sensor
Learn how to use the wait_until() function with sensors

## Slide 3: Functions YOU NEED in this lesson
Motion Sensor Functions – Used to read and reset the values of the gyro sensor
get_yaw_angle()
reset_yaw_angle()
Operator Functions – Tests a relation between two values and outputs a Boolean (true/false) result
greater_than_or_equal_to(a, b)
Wait Functions – Makes the program pause execution for some time.
wait_until(get_value_function, operator_function=<function equal_to>, target_value=True)

## Slide 4: Robot Orientation: YAW, PITCH and ROLL
Yaw is turning the Hub to right or left
Pitch is turning the Hub up and down
Roll is turning the Hub to side-to-side
Just like x, y and z coordinates are used to describe a robot’s position,
yaw, pitch and roll are terms used to describe a robot’s orientation.
Yaw is rotation around the z-axis. Pitch is rotation around y-axis.
Roll is rotation around the x-axis.
The built-in Gyro Sensor can measure the robot’s orientation

## Slide 5: Using the gyro sensor to turn
The gyro sensor can be programmed to measure the hub’s yaw, pitch and roll
These values can be used to sense if the robot has turned around x, y, or z axes
In this lesson, we will focus on yaw which can be used to determine if a robot has turned left or right
For pitch and roll, the robot uses gravity to determine what is a zero reading. Flat on the ground is 0 pitch and 0 roll.
For yaw, the robot doesn’t have a compass to tell it what is north or south. Therefore, you need to tell the robot what it should consider zero. This is done with the reset_yaw_angle() function.
  Note that clockwise is positive in yaw measurement
hub.motion_sensor.get_yaw_angle()
hub.motion_sensor.reset_yaw_angle()

## Slide 6: Challenge I
Write a program that turns 90 degrees to the right
Basic Steps:
  Make your robot start slowly turning right by just turning on the left wheel motor
    Use low speeds here to improve keep the turn accurate
  reset the gyro sensor angle to 0
  Wait until the gyro yaw angle has reached the degrees you want
  Stop moving
motor_pair = MotorPair('A', 'E')
motor_pair.set_stop_action('brake’)
motor_pair.start_tank(20, 0)
hub.motion_sensor.reset_yaw_angle()
wait_until(hub.motion_sensor.get_yaw_angle, greater_than_or_equal_to, 90)

## Slide 7: Challenge 1 Solution
motor_pair = MotorPair('A', 'E')
motor_pair.set_stop_action('brake')
motor_pair.start_tank(20, 0)
hub.motion_sensor.reset_yaw_angle()
wait_until(hub.motion_sensor.get_yaw_angle, greater_than_or_equal_to, 90)
motor_pair.stop()

## Slide 8: TURNING RIGHT Vs. TURNING LEFT
To change the direction of the turn, you have to:
  Change which wheel should turn
  The final angle should be -90 degrees instead of 90 degrees
  The comparison should be “less_than_or_equal_to“ instead of “greater_than_or_equal_to” since the angle is decreasing instead of increasing
Right Turn
Left Turn
motor_pair = MotorPair('A', 'E')
motor_pair.set_stop_action('brake’)
motor_pair.start_tank(20, 0)
hub.motion_sensor.reset_yaw_angle()
wait_until(hub.motion_sensor.get_yaw_angle, greater_than_or_equal_to, 90)
motor_pair.stop()
motor_pair = MotorPair('A', 'E')
motor_pair.set_stop_action('brake’)
motor_pair.start_tank(0, 20)
hub.motion_sensor.reset_yaw_angle()
wait_until(hub.motion_sensor.get_yaw_angle, less_than_or_equal_to, -90)
motor_pair.stop()

## Slide 9: There are two types of turns you can do
180 Degree Pivot Turn
180 Degree Spin Turn
Notice where the robot ends in both pictures after a 180 degree turn.
In the Spin Turn, the robot moves a lot less and that makes Spin Turns are great for tight positions. Spin turns tend to be a bit faster but also a little less accurate.
So when you need to make turns, you should decide which turn is best for you!
A
E
Start Position
End Position
Motors
A and E Move
A
E
Motor
A Moves
Start Position
End Position
A
E
A
E

## Slide 10: How to Make Pivot and Spin turns
Move Tank Values |  |  | 
Speed, 0 | 0, Speed | Speed, -Speed | -Speed, Speed
Pivot Turn Right | Pivot Turn Left | Spin Turn Right | Spin Turn Left
Change % Speed values here
A
E
A
E
A
E
A
E
move_tank(1, unit='rotations', 0, 50)

## Slide 11: TURNING CHALLENGES
Challenge 2
Your robot baseball player must run to second base, turn around and come back to first.
Go straight. Turn 180 degrees and return to the same spot.
A
E
Challenge 1
Your robot is a baseball player who has to run to all the bases and go back to home plate.
Can you program your robot to move forward and then turn left?
Use a square box or tape
Start and End position
First Base
A
E
Second Base

## Slide 12: CHALLENGE SOLUTIONS
Challenge 2
You probably used a spin turn because it is better for tighter turns and gets you closer to the starting point!
Challenge 1
You probably used a combination of the move() function to go straight and do pivot turns to go around the box.

## Slide 13: CREDITS
This lesson was created by Arvind Seshan for SPIKE Prime Lessons
More lessons are available at www.primelessons.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.