## Slide 1: Moving straight
Sanjay and Arvind Seshan

## Slide 2: Lesson Objectives
Learn how to make your robot go forward and backwards
Learn how to use the Move blocks

## Slide 3: Move for Duration
Simplest move block – just gives control over direction and distance
Other move blocks give control over speed and steering
Duration/Distance
Mode of operation
Set in Configuration
To use this block you will set the speed, stop mode, motor ports, wheel size (see Configuring Robot Movement Lesson)
Direction

## Slide 4: Move with Steering for Duration
This block allows you to control the move distance and turning of the robot.
This block gives control over steering by giving different amounts of power to the left and right wheels. “straight: 0” steering give equal power to both wheels, which makes the robot move straight. right:100 and left:-100 give full power to both wheels but turn them in opposite directions, which makes the robot spin right or spin left.
SPIKE Prime steering values are less gradual than the EV3. For example, right:99 and left:-99 turn one wheel and stop the other – producing a “pivot” turn. On an EV3, this required steering = 50 or -50.
Duration/Distance
Steering
Mode of operation
Set in Configuration
To use this block you will set the speed, stop mode, motor ports, wheel size (see Configuring Robot Movement Lesson)

## Slide 5: Move for Duration with Steering at Speed
This is like the move steering block. However instead of using the configured “default” speed, you specify the speed within the block.
This is useful if you have one move that you want to do more slowly or quickly.
This Block must be added to your Block Palette using Extensions. It is in the More Movement Palette.
Duration/Distance
Mode of operation
Steering
Move Speed
Set in Configuration
To use this block you will set the stop mode, motor ports, wheel size (see Configuring Robot Movement Lesson)

## Slide 6: Move for Duration at Speed (“Move Tank”)
This block allows you to control the move distance and turning of the robot.
In this block you control turning by specifying the two motor speeds independently. This is often called tank controls.
This Block must be added to your Block Palette using Extensions. It is in the More Movement Palette.
Duration/
Distance
Mode of operation
Left and Right
Wheel Speeds
Set in Configuration
To use this block you will set the stop mode, motor ports, wheel size (see Configuring Robot Movement Lesson)
In our lessons, we will use either tank controls (slide 6) or forward/backward (slide 3) since the power given to each wheel is more explicit.

## Slide 7: NEGATIVE Values
You can enter negative values for power or distance
This will make the robot move backwards
If you negate two values (e.g. power and distance, or distance and backwards direction), the robot will move forward.
Negative Power = Backwards
Positive Power = Forward
A
E
Negative Power = Backwards
Positive Power = Forward

## Slide 8: Challenge 1: Move 10 CM
Move the robot 10 centimeters forward
Basic steps:
  Configure your robot
  Use a Movement Block (Move Tank or Move For Duration block) and move forward for 10cm

## Slide 9: Challenge 1 Solution
Configure your robot
If you are using the smaller SPIKE Prime wheels on Droid Bot IV, set the one rotation to 17.5cm (image on the right)
If you are using the larger SPIKE Prime wheels on ADB, remember to set one rotation to 27.6cm
Move forward for 10 cm. The same cm mode is available in other move blocks.

## Slide 10: Challenge II: Move Forward and Back
Move your robot forward from the start line to the finish line (1) and back to the start (2)
Basic steps:
  Configure your robot
  Use a Movement Block and move forward for the desired amount (40cm)
  Use the same Movement Block to move backwards (40cm)
1
2
FINISH
START
40CM

## Slide 11: Challenge II solution
Configure your robot
If you are using the smaller SPIKE Prime wheels on Droid Bot IV, set the one rotation to 17.5cm (image on the right)
If you are using the larger SPIKE Prime wheels on ADB, you will set one rotation to 27.6cm
Robot moves forward 40cm and backwards 40cm

## Slide 12: Start Moving and Stop Moving Blocks
There are 4 more move blocks in the Movement palette.
The Start moving blocks will turn on your drive motors at the given speed (and steering if given).
These blocks have no duration/distance. After turning the motor on, the program instantly moves to the next block
The motor will continue running until stopped or controlled by another block
Stop moving will halt your drive motors no matter what action they are running.

## Slide 13: Wait blocks and Challenge iii
Since Start and Stop Moving blocks execute instantly, they need to be used with other blocks to be made useful. One common way they are used is with Wait Blocks. Wait Blocks hold up the program execution until some event occurs. The lessons on sensors cover Wait Blocks in more detail.
For now, we will use the Wait for Seconds block
This block takes the entered number of seconds to run
Challenge III:
  Use Start Moving, Stop Moving and Wait blocks to make the robot move forward for 3 seconds

## Slide 14: Challenge III: moving For 3 Seconds
Can you Move 3 Seconds using just the Start Moving and Wait blocks?
The Start Moving block starts the robot moving
After turning on the motors, the program begins running the Wait block. This takes 3 seconds to run.
The Stop Moving block makes the robot stop

## Slide 15: CREDITS
This lesson was created by Sanjay Seshan and Arvind Seshan for SPIKE Prime Lessons
More lessons are available at www.primelessons.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.