## Slide 1: Playing sound
BY ARVIND SESHAN

## Slide 2: Lesson Objectives
Learn how to use the speaker functions to play sounds

## Slide 3: Speaker Functions
Used to played beeps out of the Hub.
You can set the volume of beeps
hub.speaker.set_volume(volume)
You can read the current volume setting
hub.speaker.get_volume()
You can play a note of your choice for a particular duration
hub.speaker.beep(note=60, seconds=0.2)
You also have the option to start playing a beep, which will allow the program to continue to the next line, and then stop the beep later in the code
hub.speaker.start_beep(note=60)
hub.speaker.stop()
0-100
MIDI note number
(default value: 60)
Duration of beep
(default value: 0.2)

## Slide 4: Challenge and sample solution
Set the speaker volume to 75%
Compose a short piece of music with 4 notes
Play it 4 times
Four notes are played
Music is played 4 times using a for loop
hub.speaker.set_volume(75)
for i in range(4):
hub.speaker.beep(60, 0.25)
hub.speaker.beep(62, 0.25)
hub.speaker.beep(64, 0.25)
hub.speaker.beep(65, 0.25)
Set speaker volume to 75%

## Slide 5: CREDITS
This lesson was created by Arvind Seshan for SPIKE Prime Lessons
More lessons are available at www.primelessons.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.