## Slide 1: Introduction to distance sensor
BY ARVIND SESHAN

## Slide 2: Lesson Objectives
Learn how to use the Distance Sensor
Learn how to use the Wait Functions

## Slide 3: What is a distance sensor?
Measures the distance to an object or surface using ultrasonic technology
There are also lights around the ultrasonic sensor (4 segments) that can be programmed individually (see Lights Lesson)
The sensor can sense distances from 50-2000mm
There is a fast sensing capability from 50-300mm

## Slide 4: How do you program with a distance Sensor
The Distance Sensor must be initialized before use
distance = DistanceSensor('C')
The Distance Sensor can measure the distance to an object or surface using ultrasonic
You can also program the lights around the sensor. This is covered in a different lesson.
Units can be measured in Percent, Centimeters or Inches
Name for the sensor
Port
distance.wait_for_distance_closer_than(20, unit='cm', short_range=False)
distnace.get_distance_cm(short_range=False)
Extra feature in Python that allows you to set the mode to short_range – increases accuracy, but decreases range

## Slide 5: Challenge: Away from the Wall
You want to find the opening. Use your Distance Sensor (mounted on the side of the robot like Droid Bot IV) to locate the gap
Program your robot to move straight until it is less than 20cm from the wall
You will need to use the wait_for_distance_closer_than() function.
Pseudocode:
  Set the movement motors for your robot (A and E for ADB robot)
  Set the stop action to brake
  Set the % speed for your robot
  Initialize the distance sensor
  Start moving straight
  Use the wait for block to detect that it is less than 20cm from the wall
  Stop moving
20cm

## Slide 6: Challenge 1: Solution
motor_pair = MotorPair('A', 'E')
motor_pair.set_stop_action('brake')
motor_pair.set_default_speed(30)
distance = DastanceSensor('C')
motor_pair.start()
distance.wait_for_distance_closer_than(20, 'cm')
motor_pair.stop()
Configure robot
Start moving
Wait until the Distance sensor is less than 20cm
In previous lessons, you learnt how to configure your robot. (See Configuring Your Robot Lesson)
Stop moving

## Slide 7: extension
Once you find the wall, move the robot backwards and go through the hole

## Slide 8: CREDITS
This lesson was created by Arvind Seshan for SPIKE Prime Lessons
More lessons are available at www.primelessons.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.