## Slide 1: Introduction to Force sensor
BY ARVIND SESHAN

## Slide 2: Lesson Objectives
Learn how to use the Force Sensor
Learn how to use the Wait Functions

## Slide 3: What is a force sensor?
The Force Sensor does two main types of sensing:
  Touch sensing
  Force sensing
You can measure the Force in percent or Newtons
is_pressed()
get_force_newton()
get_force_percentage()

## Slide 4: How do you program with a force Sensor
Just like with motors, the force sensor must be initialized before use
force = ForceSensor('F')
There are two modes of the force sensor
The two modes are
  Pressed – even a gentle tap is detected
  Released – hold the sensor in and release it any amount
force.wait_until_pressed()
force.wait_until_released()
Name for the sensor
Port

## Slide 5: Challenge 1: Move until Pressed
Program your robot to move straight until you press the sensor with your hand
You will use the wait_until_pressed() function for this challenge
force.wait_until_pressed()
Basic steps:
  Set the movement motors for your robot (A and E for Droid Bot IV and ADB robot)
  Set the stop action to brake
  Set the % speed for your robot
  Initialize the force sensor
  Start moving straight
  Use the wait_until_pressed() function to detect when the Force Sensor is pressed
  Stop moving

## Slide 6: Challenge 1: Solution
motor_pair = MotorPair('A', 'E')
motor_pair.set_stop_action('brake’)
motor_pair.set_default_speed(30)
force = ForceSensor('F')
motor_pair.start()
force.wait_until_pressed()
motor_pair.stop()
In previous lessons, you learnt how to configure your robot. The first 3 lines set the movement motors, the stop action, and the default speed. (See Configuring Your Robot Lesson)
Configure robot
Start moving
Wait until the Force Sensor is pressed
Stop moving

## Slide 7: CREDITS
This lesson was created by Arvind Seshan for SPIKE Prime Lessons
More lessons are available at www.primelessons.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.